## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Out-of-Order Processing and Branch Prediction
Instructor: Siddharth Garg

## Slide 2: Lab 2 Question: Modeling Dirty Bits
You will model a two level cache hierarchy
L1
L2
Main Memory (always HIT)
Replacement policy: round-robin
Write Hit policy: write-back
Write Miss policy: no-allocate
Rd A
Rd Miss
Rd A
Rd Hit
Mem[A]
Eviction
(Wrt B)
Wrt Hit (Dirty bit updated but no further eviction)
Wrt Miss (L2 bypassed)
Observe that write-backs of dirty data from L1 cache do not result in replacements/evictions from L2. Hence, no need track of dirty bits, but you’re welcome to if you like.

## Slide 3: Tomasulo’s Algorithm
Instruction fetched in order into instruction buffer
And dispatched to reservation station assuming one is free
Instruction wait in reservation stations and monitor common data bus for operand to be available
Arch register file renamed using resv stations

## Slide 4: Tomasulo’s Algorithm
If a reservation station is available before renaming
  Instruction + renamed operands (tags/value) placed in reservation station
  If reservation station not available, STALL
While in resv stn each instruction
  Monitors CDB for tag of it’s sources
  When tag seen, grab value and keep in the reservation station
  When values for both operands available, ready for dispatch
Dispatch ready instructions to Fus
  Assuming an FU is available, otherwise wait
Once instruction completes execution
  Broadcast value and tag on CDB
  Any Register in the Reg. renaming table with a matching tag updates it value and sets valid bit
Free reservation station

## Slide 5: Exceptions
Exceptions are interrupts generated by the processor when critical events occur that require special handling
  Arithmetic overflow (recall add instruction)
  Page fault
  Mem protection violation
Out-of-order execution beyond branches can cause exceptions that would not be caused by in order execution
  If for example a branch predicted as Taken is actually Not Taken
Precise exceptions: architectural state of the processor correspond to in-order execution of program till instruction that raised exception

## Slide 6: Dealing with Exceptions in Tomasulo
Tomasulo’s algorithm does not guarantee precise exceptions
  Why? Note that Tomasulo’s algorithm updates the register file out of order
  An older instruction might raise an exception even though a younger instruction has already update the RF contents
    Or yet older instructions haven’t yet updated the RF

## Slide 7: Example
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F
D
EX
W
F: Fetch instruction
D: Decode, Rename (or DISPATCH)
E: Execute (when operands ready), multi-cycle (or ISSUE)
W: Broadcast result on CDB (or WRITEBACK)

## Slide 8: Cycle 9
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8

## Slide 9: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
~ | 8 | 1
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
~ | 2 | 1
 | .. | ..
d | .. | 0
~ | 8 | 1
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
f3 and f7 are updated, but f5 is not

## Slide 10: How to get Precise State
Force in-order completion of WB state
  Hence the architectural registers will only get updated in instruction order
  However, execution still occurs out-of-order based on true data dependencies
But, how do we keep track of
  Original instruction order
  Result of instructions that have completed execution but waiting for WB (can’t store the result in the architectural RF yet!)
  Use a new hardware structure: Re-order Buffer (ROB)

## Slide 11: Tomasulo with ROB
ROB
Instructions update ROB with results when they complete execution
RF is updated when an instruction from head of ROB commits
Instruction queued up in ROB on dispatch

## Slide 12: Tomasulo with ROB
If a reservation station AND ROB slot are available (FETCH)
  Use ROB entry (not resv station) as tag
  Instruction placed in reservation station and ROB
  else, STALL
While in resv stn each instruction (DECODE/DISPATCH)
  Monitors CDB for tag of it’s sources
  When tag seen, grab value and keep in the reservation station
  When values for both operands available, ready for dispatch
Issue ready instructions to FUs (EXECUTE/ISSUE)
  Assuming an FU is available, otherwise wait
Once instruction completes execution (WB)
  Broadcast value and tag on CDB
  Update dependent instructions in resv station and ROB with value
  Any Register in the Reg. renaming table with a matching tag updates it value and sets valid bit
  Free reservation station
Commit instruction at head of ROB (COMMIT)
  Update register file
  Free ROB

## Slide 13: Cycle 0
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | 4 | 1
 | 5 | 1
f0
f2
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
- | - | -
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
ROB

## Slide 14: Cycle 2
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | 4 | 1
A | 5 | 0
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
- | - | -
- | - | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
-
-
-
Fetch
Dispatch
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8

## Slide 15: Cycle 2
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
A | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
- | - | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
-
-
Dispatch
Issue (E1)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
-
-
-
Fetch

## Slide 16: Cycle 3
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E2)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
0
-
-
Dispatch

## Slide 17: Cycle 4
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E3)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
0
-
-
Issue (E1)

## Slide 18: Cycle 5
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E4)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
1
-
-
WB

## Slide 19: Cycle 5
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
-
-
Waiting
Issue (E4)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
1
-
-
WB

## Slide 20: Cycle 6
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 1
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
-
-
Waiting
WB
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
1
0
1
-
-
Waiting

## Slide 21: Cycle 6
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 1
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
Waiting
WB
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
1
0
1
-
-
Waiting

## Slide 22: Cycle 7
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 6 | 0
f0
f2
Tag | Value | Valid
- | 6 | 1
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
Issue (E1)
Commit
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
1
0
1
-
-
Waiting

## Slide 23: Cycle 7
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 6 | 0
f0
f2
Tag | Value | Valid
- | 6 | 1
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
Issue (E1)
Commit
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
0
1
-
-
Waiting

## Slide 24: Cycle 8
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 6 | 0
f0
f2
Tag | Value | Valid
- | 6 | 1
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
ADDD | F6 | 10
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
WB
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
1
1
-
-
Waiting

## Slide 25: Cycle 8
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 6 | 0
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
ADDD | F6 | 10
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
WB
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
1
1
-
-
Waiting

## Slide 26: Cycle 9
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
- | 10 | 1
C | 6 | 0
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
ADDD | F6 | 10
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
Commit
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
1
1
-
-
Waiting

## Slide 27: Cycle 9
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
- | 10 | 1
C | 6 | 0
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
Commit
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
-
1
-
-
Waiting

## Slide 28: Cycle 10
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
- | 10 | 1
- | 3 | 1
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
-
1
-
-
Commit

## Slide 29: Cycle 10
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
- | 10 | 1
- | 3 | 1
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
- | - | -
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
-
-
-
-
-
Commit

## Slide 30: Precise Exceptions (Cycle 4)
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E3)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
0
-
-
Issue (E1)
Causes exception

## Slide 31: Cycle 5
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
-
-
Waiting
Issue (E4)
ROB
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Valid
0
0
1
-
-
WB
Exc
0
0
1
-
-
Exception is noted in ROB, but it’s effects are deferred till commit

## Slide 32: Cycle 10
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
- | 10 | 1
- | 3 | 1
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
ROB
-
-
ROB
-
-
-
MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
Commit
Inst | Reg | Value
- | - | -
- | - | -
ADDD | F8 | 3
- | - | -
- | - | -
A
B
C
D
E
ROB
Valid
-
-
1
-
-
Exc
-
-
1
-
-
Raises exception. Note that RF contents are precise despite OoO exec.

## Slide 33: Dealing with Branches
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | 4 | 1
 | 5 | 1
f0
f2
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
- | - | -
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
ROB
Speculate past branches by predicting result of branch condition (Taken/Not)

## Slide 34: Cycle 3
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E2)
ROB
Valid
0
0
0
-
-
Dispatch
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
Fetch

## Slide 35: Cycle 4
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | -
- | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E2)
ROB
Valid
0
0
0
-
-
Dispatch
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
Fetch (and predict Not Taken)

## Slide 36: Cycle 4
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | 2 | 1
- | - | 0
Tag | Value | Valid
- | 4 | 1
- | 1 | 1
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | -
BEQ | - | -
- | - | -
A
B
C
D
E
ROB
A
-
ROB
B
C
-
Waiting
Issue (E3)
ROB
Valid
0
0
0
-
-
Issue (E1)
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
Dispatch
Fetch
T/NT
0
0
0
NT
-

## Slide 37: Cycle 5
Tag | Value | Valid
- | 3 | 1
- | - | 0
Tag | Value | Valid
- | 2 | 1
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
A | - | 0
- | - | 0
- | 2 | 1
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | 1 | 1
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | -
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
SUBD | F4 | -
A
B
C
D
E
ROB
A
-
ROB
B
-
E
Waiting
Issue (E4)
ROB
Valid
0
0
1
-
0
WB
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
Issue (E1)
Dispatch
T/NT
0
0
0
NT
-

## Slide 38: Cycle 6
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 0
- | - | 0
- | 2 | 1
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | 1 | 1
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
SUBD | F4 | -
A
B
C
D
E
ROB
-
-
ROB
B
-
E
Waiting
WB
ROB
Valid
0
0
1
-
0
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-

## Slide 39: Cycle 6
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 0
- | - | 0
- | - | -
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | -
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
SUBD | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
Waiting
WB
ROB
Valid
0
0
1
-
-
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-
Anything else?

## Slide 40: Cycle 6
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 0
- | - | 0
- | - | -
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | -
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
SUBD | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
Waiting
WB
ROB
Valid
0
0
1
-
-
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-
Undo renaming in RF

## Slide 41: Hardware Branch Prediction
Hardware branch predictor has two tasks
  Determine if branch is taken or not-taken
  Target address calculation (where to go if taken)
  Target address calculation also required for unconditional branches (jumps)
Past predicts the future.
  Local History: If branch was taken the previous time, it will probably be taken subsequently (why?)
  Global History: taken/not-taken behavior of other branches can be predictive for current branch (why?)

## Slide 42: Local History Prediction
For each branch, predict based on whether the branch was previously T/NT
  If previously Taken, then branch is Taken
  Pattern: T, T, T, NT, T, T, T, T, ….
  The NT branch will be predicted as T and the next T branch as NT
  Even worse if pattern is: T, NT, T, NT, ….
Sticky prediction: wait for two mispredictions to change prediction from T to NT and vice-versa

## Slide 43: 2-bit Saturating Counter
Predict Taken
(11)
Predict Taken
(10)
Taken
Not Taken
Predict
Not Taken
(01)
Taken
“Strong Confidence
In Taken”
“Weak Confidence
In Taken”
“Weak Confidence
In Not Taken”
Taken
Predict
Not Taken
(00)
Not Taken
Taken
Not Taken
Not Taken
“Strong confidence in Not Taken”
Two bits of state required to implement FSM

## Slide 44: Branch Prediction Buffer
Hardware structure that is looked-up during fetch stage to determine Taken/Not Taken
32-bit Program Counter
m bits
2m Entries
2 bit saturating counter
Taken/Not Taken
Ideally, one 2-bit saturating counter per PC but that is too expensive
Why m LSBs and not MSBs?

## Slide 45: Correlating Predictors
2-bit scheme looks at each branches own prior behavior to make predictions
  But branch behavior can be correlated
If (aa==2) aa=0;
If (bb==2) bb=0;
If (aa==bb) {.…}
If first two branches are taken, the third branch MUST be taken
k-bit global branch history register (BHR)
T
NT
k=2 BHR
(Prev branch was NT,
branch before that was T)

## Slide 46: 2-Level Correlation Predictors
Assume k=2
32-bit Program Counter
m bits
2m
s=2 bit saturating
counter
Taken/
Not Taken
T
NT
k=2 BHR
Pattern History Table (PHT)