## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Branch Prediction and Miscellaneous
Instructor: Siddharth Garg

## Slide 2: Hardware Branch Prediction
Hardware branch predictor has two tasks
  Determine if branch is taken or not-taken
  Target address calculation (where to go if taken)
  Target address calculation also required for unconditional branches (jumps)
Past predicts the future.
  Local History: If branch was taken the previous time, it will probably be taken subsequently (why?)
  Global History: taken/not-taken behavior of other branches can be predictive for current branch (why?)

## Slide 3: Local History Prediction
For each branch, predict based on whether the branch was previously T/NT
  If previously Taken, then branch is Taken
  Pattern: T, T, T, NT, T, T, T, T, ….
  The NT branch will be predicted as T and the next T branch as NT
  Even worse if pattern is: T, NT, T, NT, ….
Sticky prediction: wait for two mispredictions to change prediction from T to NT and vice-versa

## Slide 4: 2-bit Saturating Counter
Predict Taken
(11)
Predict Taken
(10)
Taken
Not Taken
Predict
Not Taken
(01)
Taken
“Strong Confidence
In Taken”
“Weak Confidence
In Taken”
“Weak Confidence
In Not Taken”
Taken
Predict
Not Taken
(00)
Not Taken
Taken
Not Taken
Not Taken
“Strong confidence in Not Taken”
Two bits of state required to implement FSM

## Slide 5: Branch Prediction Buffer
Hardware structure that is looked-up during fetch stage to determine Taken/Not Taken
32-bit Program Counter
m bits
2m Entries
2 bit saturating counter
Taken/Not Taken
Ideally, one 2-bit saturating counter per PC but that is too expensive
Why m LSBs and not MSBs?

## Slide 6: Example
Consider a m=3 and assume that all counters start in 11 state
  8 2-bit counters indexed from 0…7
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
8 Entries
2 bit saturating counter
Taken/Not Taken
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
101

## Slide 7: Branch 1
Index into table and predict branch outcome
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
8 Entries
2 bit saturating counter
Predict Taken
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
000

## Slide 8: Branch 1
Update counter once actual branch outcome is known
1 | 0
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
8 Entries
2 bit saturating counter
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
000

## Slide 9: Branch 2
Index into table and predict
1 | 0
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
Predict Taken
2 bit saturating counter
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
001

## Slide 10: Branch 2
Update counter
1 | 0
1 | 1
1 | 0
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
2 bit saturating counter
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
001

## Slide 11: Branch 3
Index into table and predict and update counter
1 | 0
1 | 1
1 | 0
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
2 bit saturating counter
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
111
Predict Taken

## Slide 12: In-Class Exercise
For each branch, determine if it was predicted as T/NT and determine the final values stored in the branch prediction buffer
1 | 0
1 | 1
1 | 0
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
2 bit saturating counter
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N Predict T
0x00000002 N Predict T
0x00000007 T Predict T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N

## Slide 13: Solution
Note that you can determine the outcome for each branch separately
1 | 1
1 | 1
0 | 0
1 | 1
1 | 1
1 | 1
1 | 1
0 | 0
32-bit Program Counter
3 bits
2 bit saturating counter
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N Predict T
0x00000002 N Predict T
0x00000007 T Predict T
0x00000000 T Predict T
0x00000002 N Predict T
0x00000007 N Predict T
0x00000000 T Predict T
0x00000002 N Predict N
0x00000007 N Predict T

## Slide 14: Correlating Predictors
2-bit scheme looks at each branches own prior behavior to make predictions
  But branch behavior can be correlated
If (aa==2) aa=0;
If (bb==2) bb=0;
If (aa==bb) {.…}
If first two branches are taken, the third branch MUST be taken
k-bit global branch history register (BHR)
T
NT
k=2 BHR
(Prev branch was NT,
branch before that was T)

## Slide 15: 2-Level Correlation Predictors
Assume m=3, k=2
32-bit Program Counter
3 bits
s=2 bit saturating
counter
Taken/
Not Taken
T
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N

## Slide 16: Branch 1
Assume all counters start at 11, and BHR is initialized to NT, NT
1 | 1
32-bit Program Counter
3 bits
Predict Taken
NT
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N

## Slide 17: Branch 1
Update PHT
1 | 0
32-bit Program Counter
3 bits
Predict Taken
NT
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N

## Slide 18: Branch 2
Update BHR, Index into PHT
1 | 0
1 | 1
32-bit Program Counter
3 bits
Predict Taken
NT
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 19: Branch 2
Update PHT
1 | 0
1 | 0
32-bit Program Counter
3 bits
Predict Taken
NT
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 20: Branch 3
Update BHR, Index into PHT
1 | 0
1 | 0
1 | 1
32-bit Program Counter
3 bits
Predict Taken
NT
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 21: Branch 3
Update PHT
1 | 0
1 | 0
1 | 1
32-bit Program Counter
3 bits
Predict Taken
NT
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 22: Branch 4
Update BHR, Index into PHT
1 | 0
1 | 0
1 | 1
32-bit Program Counter
3 bits
Predict Taken
1 | 1
T
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 23: Branch 4
Update PHT
1 | 0
1 | 0
1 | 1
32-bit Program Counter
3 bits
Predict Taken
1 | 1
T
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 24: In-Class Exercise
Determine the predictions for all branches and state of PHT
1 | 0
1 | 0
1 | 1
32-bit Program Counter
3 bits
1 | 1
T
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N
0x00000002 N
0x00000007 T
0x00000000 T
0x00000002 N
0x00000007 N
0x00000000 T
0x00000002 N
0x00000007 N
older
younger

## Slide 25: Solution
Determine the predictions for all branches and state of PHT
1 | 1
1 | 0
1 | 1
32-bit Program Counter
3 bits
0 | 0
1 | 1
1 | 0
1 | 0
T
NT
k=2 BHR
Pattern History Table (PHT)
Branch Trace <PC, T/NT>
0x00000000 N Predict T
0x00000002 N Predict T
0x00000007 T Predict T
0x00000000 T Predict T
0x00000002 N Predict T
0x00000007 N Predict T
0x00000000 T Predict T
0x00000002 N Predict T
0x00000007 N Predict T
older
younger

## Slide 26: Conflicts in PHT
Two branches use the same counter!
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
1 | 1
32-bit Program Counter
3 bits
8 Entries
2 bit saturating counter
Predict Taken
0
1
2
3
7
Branch Trace <PC, T/NT>
0x00000000 N
0x20000000 N
0x00000007 T
0x00000000 T
0x20000000 N
0x00000007 N
0x00000000 T
0x20000000 N
0x00000007 N
000

## Slide 28: Dealing with Branches
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | 4 | 1
 | 5 | 1
f0
f2
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 0
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
- | - | -
- | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
-
ROB
Speculate past branches by predicting result of branch condition (Taken/Not)

## Slide 29: Cycle 6
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 0
- | - | 0
- | 2 | 1
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | 1 | 1
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
SUBD | F4 | -
A
B
C
D
E
ROB
-
-
ROB
B
-
E
Waiting
WB
ROB
Valid
0
0
1
-
0
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-

## Slide 30: Cycle 6
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 0
- | - | 0
- | - | -
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | - | -
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
B
-
-
Waiting
WB
ROB
Valid
0
0
1
-
-
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-
Anything else?

## Slide 31: Cycle 6
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
-- | - | -
A
B
C
D
E
Waiting
WB
ROB
Valid
0
0
1
-
-
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-
Undo renaming in RF
Clear tags and step through ROB from head up to the branch instruction
Tag for F8 Should be A
Tag for F6 Should be B
Tag for F8 Should be C

## Slide 32: Cycle 6
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
B | 4 | 0
C | 5 | 0
f0
f2
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
-- | - | -
A
B
C
D
E
Waiting
WB
ROB
Valid
0
0
1
-
-
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
T/NT
0
0
0
NT
-
Undo renaming in RF
Clear tags and step through ROB from head up to the branch instruction
Tag for F8 Should be A
Tag for F6 Should be B
Tag for F8 Should be C

## Slide 33: Another Alternative
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
B | 4 | 0
C | 5 | 0
f0
f2
Tag | Value | Valid
- | 6 | 0
- | - | 0
- | 2 | 1
Tag | Value | Valid
- | 4 | 1
- | - | 0
- | 1 | 1
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
MULD | F8 | 6
ADDD | F6 | -
ADDD | F8 | 3
BEQ | - | -
SUBD | F4 | -
A
B
C
D
E
ROB
-
-
ROB
B
-
E
Waiting
WB
ROB
Valid
0
0
1
-
0
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
CONTINUE TILL BRANCH REACHES HEAD OF ROB
T/NT
0
0
0
NT/T
-

## Slide 34: In The Future
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
E | 3 | 0
 | smthg | 1
 | smthg | 1
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | 2 | 1
Tag | Value | Valid
- | - | 0
- | - | 0
- | 1 | 1
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
- | - | -
BEQ | - | -
SUBD | F4 | smthg
A
B
C
D
E
ROB
-
-
ROB
-
-
E
Waiting
WB
ROB
Valid
-
-
-
-
1
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
CONTINUE TILL BRANCH REACHES HEAD OF ROB
T/NT
--
--
-
NT/T
-

## Slide 35: In The Future
Tag | Value | Valid
- | - | 0
- | - | 0
Tag | Value | Valid
- | - | 0
- | - | 0
FP MULT (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
- | 3 | 1
 | smthg | 1
 | smthg | 1
f0
f2
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | 1
Tag | Value | Valid
- | - | 0
- | - | 0
- | - | -
FP ADD (1 cycles)
f4
f6
f8
Inst | Reg | Value
- | - | -
- | - | -
- | - | -
BEQ | - | -
- | - | -
A
B
C
D
E
ROB
-
-
ROB
-
-
E
Waiting
WB
ROB
Valid
-
-
-
-
-
Waiting
L1: MULD F4, F2, F8
ADDD F8, F6, F6
ADDD F2, F0, F8
BEQ R1, R2, L1
SUBD F2, F0, F4
BRANCH TAKEN (Oops!)
Issue (E1)
KILL ALL INSTRUCTIONS THAT OCCUR AFTER BRANCH IN ROB
T/NT
--
--
-
NT/T
-

## Slide 36: Tomasulo’s Algorithm (Loads/Stores)
Loads queue up in the load buffer. Serves as parent for other instructions
Stores queue up in the store buffer. Parents for loads
In Tomasulo’s original design, the address of load/store is computed during issue stage

## Slide 37: Tomasulo’s Algorithm (Loads/Stores)
Question: can loads be directly dispatched to the L1 cache?
Stores queue up in the store buffer. Parents for loads
Look up store buffer first for older store instructions with the same address!

## Slide 38: Tomasulo’s Algorithm (Loads/Stores)
Question: what happens when the result of load is returned?
Stores queue up in the store buffer. Parents for loads
Broadcast on CDB for dependent instructions to consume

## Slide 39: Tomasulo’s Algorithm (Loads/Stores)
Question: what happens when the result of load is returned?
When is a store ready to execute?
When the value it needs to store is available