## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Single Cycle MIPS Implementation
Instructor: Siddharth Garg

## Slide 2: MIPS ISA Overview
32-bit ISA (what does this mean?)
  Instruction length: 32 bits
  Data word length: 32 bits
32 general purpose registers ($0, $1, $2, … $31); 32-bits each
  Register $0 is hard-wired to 0 (constant)
  All other registers can be used as read/write
  But, certain registers dedicated for specific purposes by compiler
    Global pointer ($28), Stack pointer ($29), Frame pointer ($30), Return Address ($31)
    We wont worry about these conventions in this class!
Two dedicated 32-bit registers hi and lo for multiplication ops
Separate regs/unit for floating point ops (discussed later)

## Slide 3: MIPS Instructions: R-Type
add rs, rt, rd // R[rd] ← R[rs] + R[rd]; signed addition; trap on overflow
sub rs, rt, rd // R[rd] ← R[rs] - R[rt]; signed subtraction; trap on overflow
or rs, rt, rd // R[rd] ← R[rs] | R[rt]; bit-wise Boolean OR operation
sll rt, rd, shamt // R[rd] ← R[rt] << shamt; logical shift left
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Add: 100000 = 20hex
Sub: 100010 = 22hex
Or: 100101 = 25hex
Sll: 000000 = 00hex

## Slide 4: 2’s Complement Representation
add rs, rt, rd // R[rd] ← R[rs] + R[rd]; signed addition; trap on overflow
rs, rt and rd are assumed to contain 32-bit signed, 2’s complement numbers
Example using 4-bit signed complement numbers ([-8,7])
Overflow occurs when result lies outside [-8,7]
1 1 0 1 = -1*23 + 1*22 + 0*21 + 1*20 = -8 + 4 + 0 + 1 = -3
+ 1 1 0 1 = 0*23 + 1*22 + 0*21 + 1*20 = 0 + 4 + 0 + 1 = -3
-----------
1 1 0 1 0 = 0*23 + 0*22 + 1*21 + 0*20 = 0 + 0 + 2 + 0 = 2
Carry out
bit is dropped

## Slide 5: MIPS Instructions: I-Type
addi rs, rt, imm // R[rt] ← R[rs] + {SignExtend, imm}; MSB of imm is extended to 32 bits
beq rs, rt, imm // if{R[rs] == R[rt]} branch to PC + 4 + imm; (“PC relative”)
ori rs, rt, imm // R[rt] ← R[rs] | {ZeroExtend,imm}; bit-wise Boolean OR operation
lw rs, rt, imm // R[rt] ← Mem[ {SignExtendimm} + R[rs] ] (“Displaced/based”)
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0
Operand register
Immediate operand
addi: 8hex
beq: 4hex
ori: 25hex
lw: 23hex
Result register
(“PC relative”)

## Slide 6: Sign Extending Immediate Operand
R[rs] has 32-bits, but imm has only 16-bits.
Example of sign extension when R[rs] has 4 bits and Imm has 2 bits
addi rs, rt, imm // R[rt] ← R[rs] + {SignExtend, imm}; MSB of imm is extended to 32 bits
1 1 0 1 = -3
+ ? ? 0 1 = +1
-----------
SignExtend
1 1 0 1 = -3
+ 0 0 0 1 = +1
-----------
1 1 0 1 = -3
+ ? ? 1 1 = -1
-----------
SignExtend
1 1 0 1 = -3
+ 1 1 1 1 = -1
-----------

## Slide 7: MIPS Instructions: J-Type
j address // PC ← {PC+4[31:28], address, 00}
(Error in Lecture 2)
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
Immediate operand
j: 2hex
jal: 3hex

## Slide 8: Implementation of the MIPS ISA
Hardware building blocks
PC
Program Counter
A 32-bit “register”
(can store information)
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
Wrt Enable
Register File
32 32-bit registers
(2 Read ports, 1 Write Port)
5 bit address
5 bit address
5 bit address
32 bit data
32 bit data
32 bit data
Set to ‘1’ to enable write
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
Wrt Enable
.
.
00000
00001
00010
00011
11111
A21F FFB3
0000 0000
BB33 CD53
1242 221E
0001 0001
ADDRESS
DATA
00001
11111
0
A21F FFB3
0001 0001
FFFF FFFF
00010
1
FFFF FFFF
00010
FFFF FFFF

## Slide 9: Arithmetic Logic Unit
result
ALU op
? bits
oprnd1
oprnd2
32 bits
32 bits
32 bits
Add: 20hex
Addu: 21hex
Sub: 23hex
Subu: 24hex
And: 25hex
Or: 24hx
Nor: 27hex
Arithmetic/Logic Unit (ALU)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Inst[2:0] decides which operation the ALU performs.
3
In-Class Problem 1: how do we set the bits of ALUop?

## Slide 10: Implementation of the MIPS ISA
Hardware building blocks
Is this a von Neumann architecture?
Read Address
Instruction
Instruction Memory
(Read only)
32 bits
32 bits
Address
Write
Data
Read Data
Data Memory
Read Mem
Write Mem
32 bits
32 bits
32 bits
Set to ‘1’ to enable read; 0 otherwise
Set to ‘1’ to enable write; 0 otherwise
Data Memory
(Either read or write, but not both together)

## Slide 11
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
R-Type ALU Instructions
“Datapath”

## Slide 12
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
Example: Instruction at PC=0
000000
00001
.
.
00000
00001
00010
00011
11111
A21F FFB3
0000 0000
BB33 CD53
1242 221E
0001 0001
RF Contents
00010
00011
00000
010100
00001
00010
00011
0
A21F FFB3
BB33 CD53
1
0
4
4
A21F FFB3 | BB33 CD53

## Slide 13
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
I-Type ALU Instructions
20:16
Sign
Extend
15:0
32

## Slide 14
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
15:11
Adder
+4
ALU op
3
Wrt Enable
1
Combined R-Type and
I-Type ALU Instructions
20:16
Sign
Extend
15:0
MUX
a
b
control
a if (control = 1)
b if (control = 0)
I-Type?
I-Type?

## Slide 15
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = ?
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
Read Mem
Write Mem

## Slide 16
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
IsLoad?
0

## Slide 17
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
1
I-Type Store Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
In-Class Problem 2:
Did we miss something?
0
sw rs, rt, imm //M[R[rs]+SignExtendimm] ← R[rt]

## Slide 18
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
!(IsStore?)
Final Data-Path
(Excluding Control Flow Instructions)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?

## Slide 19: Control Flow
J-Type Control Flow
  4 MSB bits taken from the 4 MSBs of PC+4
  Next 26 bits taken from the “address” field
  Last 2 bits are set to zero? (why?)
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
j address // PC ← {PC+4[31:28], address, 00}, opcode=2hex
(Erroneous in Lec. 2 notes, please update)

## Slide 20
PC
Read Address
Instruction
Instruction Memory
Adder
+4
J-Type Control Instruction
RF Onwards Not Shown
Concat
31:28
PC+4
25:0
00
J-Type?
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
15:0
I-Type?
!(IsStore?)
What about WrtEnable?
0
!(J-Type?)

## Slide 21: Control Flow
I-Type Branch Instruction
  First 30 MSBs from sign extended immediate
  2 LSBs are always 0
beq rs, rt, imm // If (R[rs]==R[rt])
// PC ← PC + 4 + {SignExtendImm, 00},
// else
// PC ← PC + 4
// opcode=4hex
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0

## Slide 22
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
Sign
Extend
15:0
I-Type?
I-Type?
PC
Read Address
Instruction
Instruction Memory
Adder
+4
Concat
31:28
PC+4
25:0
00
NextPC? = function(J-Type?, IsBranch?, IsEq?)
Adder
PC+4
=
IsEq?
{SignExtendImm[29:0],00}
29:0
!(IsBranch?)
3:1 MUX

## Slide 23
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Generating Control Signals
(Control Path)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
ALUOp
IsLoad?
IsStore?
I-Type?
Wrt Enable

## Slide 24
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
ALUOp
IsLoad? = (Inst[31:26] == 100011)
IsStore? = (Inst[31:26] == 101011)
I-Type? = (Inst[31:26] != 00000) && (Inst[31:26] != 00010)
Wrt Enable

## Slide 25
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
If (Inst[31:26] == 100011) | (Inst[31:26] == 101011)
ALUop = 001
Else
ALUop = Inst[2:0]
ALUOp

## Slide 26
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
If (IsStore? | IsBranch? | J-Type?)
WrtEnable = 0
Else
WrtEnable = 1
WrtEnable
J-Type? = (Inst[31:26]==000010)
IsBranch? = (Inst[31:26]==000100)

## Slide 27
If (IsBranch? && isEQ?)
NextPC? = 2
else if (J-Type?)
NextPC? = 1
else
NextPC? = 0
In-Class Problem 3:
Write pseudo-code for NextPC?