## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Caches
Instructor: Siddharth Garg

## Slide 2: 5 Stage Pipeline (with support for load/store)
Two forwarding paths
  Same destination register in both forwarding paths? Pick data from EX-EX forwarding path
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Forwarding Control Logic
R[rd] from prior instruction
R[rd] from prior to prior instruction

## Slide 3: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
EX-EX Forwarding

## Slide 4: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4

## Slide 5: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Will this work?
Solution: Stall the pipeline

## Slide 6: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Solution: Stall the pipeline
EX
R[$4] + R[$5]

## Slide 7: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding

## Slide 8: RAW Hazards: Load-Store Dependency (NEW)
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
R[$4] = Mem[Addr]
WB
Write $4
IF
ID/RF
EX
MEM
sw $5, $4, imm
Read $5
Mem[Addr] = R[$4]
WB
Write $9
MEM-MEM Forwarding (new)
Addr = R[$5] + SgnImm

## Slide 9: 5 Stage Pipeline (with support for load/store)
Three forwarding paths
  EX-EX, MEM-EX, MEM-MEM
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Forwarding Control Logic
R[rd] from prior to prior instruction

## Slide 10: 5-Stage Pipeline
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Note: simplified pictures of IF and MEM stages
How are Imem and Dmem implemented?

## Slide 11: Memory System
ID/RF
(Decoder, RF)
EX
(ALU)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Memory Controller
Processor
Main Memory
Dynamic Random Access Memory (DRAM)
(Unified instruction and data memory)

## Slide 12: DRAM Details
ID/RF
(Decoder, RF)
EX
(ALU)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Memory Controller
3.6 GHz Pentium 4
Main Memory
Memory capacity: 4GB
Access Latency: 50 ns/word = ?? Clock cycles/word
= 50 ns / (1/3.6) ns = 180 cycles

## Slide 13: Memory Technologies
 | DRAM | SRAM (512 KB) | SRAM (4 MB)
Cell | 1 Transistor, 1 Capacitor (1T-1C) | 6 Transistor (6T) | 6 Transistor (6T)
Density (bits/um2) | High | Low | Low
Access Latency (ns) | Large | Small | Medium

## Slide 14: Memory Hierarchy
Decoder, RF, EX
SRAM
L1 Cache
SRAM
L2 Cache
CPU
DRAM Main Memory
Cache = “temporary storage space”
Instead of slow off-chip access to large DRAM, store frequently used data in on-chip SRAM cache
Hierarchy:
L1 Cache: small (32 KB), very fast (typically 1 clock cycle)
L2 Cache: larger (1 MB), slower (10s of nsecs)
L3 Cache: even larger ….
Main Memory: 4GB, 100s of nsecs

## Slide 15: Locality
Decoder, RF, EX
SRAM
L1 Cache
SRAM
L2 Cache
CPU
DRAM Main Memory
Temporal locality: if you’ve accessed some data, you’ll likely access it again in the near future
  Same instructions are repeatedly accessed within loops
  For example the loop counter
Spatial locality: if you’ve accessed some data, you’ll likely access nearby data
  Array accesses
  Instruction are accessed in sequential order

## Slide 16: Access Pattern Exhibiting Locality
http://www.eetimes.com/document.asp?doc_id=1275470

## Slide 17: Cache Organization
Caches store data in chunks of “cache blocks”
  Access to a cache returns an entire cache block
  A block can be as small as 1 byte, but can be larger (example: 4 bytes)
32 KB cache
1 Byte cache block
i.e., 32768 blocks
32 bit address
from CPU
Where does a block go when it is fetched into cache? (Placement)
How do we know if a block already exists in the cache? (Identification)
Which block should we kick out if there isn’t enough room? (Replacement)

## Slide 18: Direct Mapped Cache
Assume 32 KByte cache with a 1 Byte cache block
32 bit address
from CPU
Block 0
Block 1
Block 2
Block 32767
Address 0, 32768, 2*32768, …
Address 1, 32769, 2*32768+1, …
Address 2, 32770, 2*32768+2, …
Address 32767, 65535, …
1 Byte = 8 bits

## Slide 19: Direct Mapped Cache: Placement
Each block in the cache has a log2(32768) = 15 bit “index”
32 bit address
from CPU
Block 0
Block 1
Block 2
Block 32767
Address 0, 32768, 2*32768, …
Address 1, 32769, 2*32768+1, …
Address 2, 32770, 2*32768+2, …
Address 32767, 65535, …
Index
Index
(15 bits)
15 LSBs of address are used to look up (index) into the cache

## Slide 20: Direct Mapped Cache: Identification
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Addr 0
Addr 32768
0….00
0…………………….01
Addr ….
0….00
1…………………….11
Data Array
(8 bits)
How do we know which block of data is stored?
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)

## Slide 21: Direct Mapped Cache: Replacement
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Access 1
Access 3
0….00
0…………………….01
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)
Data[0]
Hit
0…………… 00
Data[32768]
0…………… 01
0….00
0…………………….00
Access 2
Miss
Miss
Access 4
0….01
0…………………….00
Miss
Data[32769]
0…………… 00

## Slide 22: Direct Mapped Cache: Replacement
32 bit address
Block 0
Block 1
Block 2
Block 32767
Index
(15 bits)
0….00
0…………………….00
Access 1
Access 3
0….00
0…………………….01
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
Tag
(17 bits)
Data[0]
Hit
0…………… 00
Data[32768]
0…………… 01
0….00
0…………………….00
Access 2
Miss
Miss
0
0
0
Valid
(1 bit)
1
1
Data[32769]

## Slide 23: Cache Operation
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address (32 bits)
V 2
=
MISS
0
&
1
0
HIT
1
Output Data if HIT

## Slide 24: Alternative Placement
Assume 32 KByte cache with a 1 Byte cache block
Block 0
Block 1
Block 2
Block 32767
Address 0, 1, 2, 3, …..
Address 32678, ….
1 Byte = 8 bits
Use 15 MSBs of address to determine index
Consider following stream of accesses:
Addr 0, Addr 1, Addr 0, Addr 1,..
“Conflict Misses”
Bad Idea!

## Slide 25: Set Associative Caches
Direct mapped caches can have high conflict miss rate
  Each address maps to a unique location in the cache
Assume addresses A and B with same index bits
  Sequence: A, B, A, B, A….. results in 100% cache miss rate!
Set-associative cache: each address can map to N different locations in the cache!
  “N-way” set associative cache
  2-way set associate cache has ~0% cache miss rate for sequence A, B, A, B …

## Slide 26: 2-Way Set Associative Cache
2-way set-associative 32 KB cache with 1 Byte blocks
Set 0
Data Array
(8 bits)
Tag Array
(? bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(? bits)
Set 1
Set 16384
Way 0
Way 1

## Slide 27: Placement
Set 0
Data Array
(8 bits)
Tag Array
(? bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(? bits)
Set 1
Set 16384
Way 0
Way 1
Index
(? bits)
Tag
(? bits)
Data mapped to a unique set but can be placed in either way
Index
(14 bits)
Tag
(18 bits)

## Slide 28: Identification
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
=
&
HIT?
=
&
HIT?

## Slide 29: Replacement
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
Sequence: A B B A A A A C
M
Data[A]
Tag[A]
1
M
Data[B]
Tag[B]
1
H
H
H
H
H
M
Where should C go?
(Addresses A, B, C map to same set)

## Slide 30: Least Recently Used (LRU)
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
Sequence: A B B A A A A C
M
Data[A]
Tag[A]
1
M
Data[B]
Tag[B]
1
H
H
H
H
H
M
Replace least recently used block
Data[C]
Tag[C]
Evicted!

## Slide 31: Implementing LRU
Data Array
(8 bits)
Tag Array
(18 bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(18 bits)
Way 0
Way 1
Sequence: A B B A A A A C
M
Data[A]
Tag[A]
1
M
Data[B]
Tag[B]
1
H
H
H
H
H
M
MRU
(1 bit)
0
1
0
LRU = NOT MRU

## Slide 32: Practical LRU Implementation
LRU is hard to implement in hardware for N>2
  Keep track of all possible N! orderings of N ways
  A linked list in which the head points to MRU and tail points to LRU
  Example: N=4; 4 x 2 bits = 8 bits per cache set and extra logic to update list on every access
Alternative policies that are more hardware friendly
  NOT MRU: same as LRU for N=2, requires only log(N) bits, easy update
  Hierarchical: for N=4, divide ways into 2 groups of 2 ways

## Slide 33: Hierarchical LRU Implementation
Way 0
Way 1
Way 2
Way 3
Group 0
Group 1
A
B
C
D
MRU Grp
MRU Way (G1)
MRU Way
(G0)
Sequence | A | C | D | B | A | A | E
MRU Grp | 0 | 1 | 1 | 0 | 0 | 0 | 
MRU Way (G0) | 0 | 0 | 0 | 1 | 0 | 0 | 
MRU Way (G1) | - | 2 | 3 | 3 | 3 | 3 | 
Which block is evicted?

## Slide 34: Hierarchical LRU Implementation
Way 0
Way 1
Way 2
Way 3
Group 0
Group 1
A
B
C
D
MRU Grp
MRU Way (G1)
MRU Way
(G0)
Sequence | A | C | D | B | A | D | E
MRU Grp | 0 | 1 | 1 | 0 | 0 | 1 | 
MRU Way (G0) | 0 | 0 | 0 | 1 | 0 | 0 | 
MRU Way (G1) | - | 2 | 3 | 3 | 3 | 3 | 
Which block is evicted?
Not the true LRU block!