## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Virtual Memory + Caches
Instructor: Siddharth Garg

## Slide 2: 32 KB Direct Mapped Cache with 1 Byte Blocks
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address (32 bits)
V 2
=
MISS
0
&
1
0
HIT
1
Output Data if HIT

## Slide 3: 32 KB 2-Way Set Associate Cache
Set 0
Data Array
(8 bits)
Tag Array
(? bits)
Valid
(1 bit)
Data Array
(8 bits)
Valid
(1 bit)
Tag Array
(? bits)
Set 1
Set 16384
Way 0
Way 1
Index
(? bits)
Tag
(? bits)
Data mapped to a unique set but can be placed in either way
Index
(14 bits)
Tag
(18 bits)

## Slide 4: Multi-Level Caches
L1-I
Instructions only
Unified L2
Both instructions and data
L1-D
Data Only
Partitioned L1-I and L1-D cache
  Reminiscent of Harvard architecture
  Why is this useful?
Inclusive vs. exclusive cache hierarchy
  Inclusive: everything in the L1-I and L1-D caches is also in the L2 cache, but not vice-versa
    Miss in L1 fetches data into both L2 and L1
    Eviction from L1 need not evict from L2
    Eviction from L2 must also evict from L1
    What if L2 block size is larger than L1 block size?
Larger, higher associativity, larger block size

## Slide 5: Software Techniques
Data layout and access patterns can have a significant impact on cache miss rate
  Code can be re-written to exploit the underlying cache hierarchy
  Caution: Might need to be aware of cache parameters
Examples of code optimization to improve cache miss rate:
  Array merging: interleaving the layout of concurrently accessed arrays
  Loop re-ordering
  Blocking

## Slide 6: Array Merging
int a[2048]
int b[2048]
int c[2048]
//Assume every int is 4 Bytes
for (i=0; i<2048; i++)
c[i] = a[i] + b[i];
Block 0
Block 4072
Data Array
(16 bytes)
Block 1
struct merge{
int a;
int b;
int c;
};
struct merge abc[2048]

## Slide 7: Loop Interchange
for (i=0; i<2048; i++)
for (j=0; i<2048; i++)
sum+= a[j][i];
//Arrays stored in column major order
//a[0][0]
//a[0][1]….
//a[1][0] …
Block 0
Block 4072
Data Array
(16 bytes)
Block 1
for (j=0; i<2048; i++)
for (i=0; i<2048; i++)
sum+= a[j][i];

## Slide 8: Blocking
for (i=0; i<N i++)
for (j=0; j<N; j++)
for (k=0; k<; k++)
sum = sum + a[i][k]*b[k][j];
a[0][0]
b[0][1]
a[1][0]
a[0][N-1]
b[0][0]
a[0][1]
b[1][0]
Same elements are being repeatedly reused!
If N is large, by the time the loop gets to a[0][N-1], a[0][0] has been evicted from the cache

## Slide 9: Blocking
a[0][0]
b[0][0]
Partition matrix into B*B sub-blocks such that the sub-blocks fit in the cache
B
B
B
B

## Slide 10: Virtual Memory
A 32-bit address allows each program to access 4GB of main memory
  What if the DRAM is smaller than 4GB?
Virtual memory: addresses that a program don’t refer to actual physical locations in main memory
CPU
Main Mem.
(DRAM)
< 4GB
Hard Disk
(Denser than DRAM, but slow)
> 4GB

## Slide 11: Virtual Memory
0…00
0…01
1…10
Virtual Addresses
(32 bits)
4GB Virtual Address Space
00
01
Physical Addresses
(2 bits)
TINY 4B Main Memory!
0…10
10
11
1…11
Large Disk
Anything does not fit in main memory is stored on disk

## Slide 12: Virtual Memory
0…00
0…01
1…10
Virtual Addresses
(32 bits)
4GB Virtual Address Space
00
01
Physical Addresses
(2 bits)
TINY 4B Main Memory!
0…10
10
11
1…11
Large Disk
Anything does not fit in main memory is stored on disk

## Slide 13: Pages
0
4KB Page
32 Bit Addresses
Virtual address space is partitioned into chunks called “pages”
  Typical page size: 4KB (212 Bytes)
  Address space: 4GB = 4GB/4KB (232/ 212)= 1M (220) pages
1
4095
4096
8191
4097
4KB Page
232-1
4KB Page
Page Offset
(12 bits)
Virtual Page Number
(20 bits)
Virtual Address (32 bits)
Selects a page
Selects a byte within a page

## Slide 14: Virtual Memory
Virtual Address Space
(4GB = 1M Pages)
Physical Addresses
(14 bits)
8 KB Main Memory
(2 Pages)
Large Disk
Pages that do not fit in main memory are stored on disk
4 KB
4 KB
Bytes within a page are mapped contiguously
Page Table
Virtual Page Number | Physical Page Num (1 bit) | Valid Bit
0 | 0 | 1
1 |  | 0
2 |  | 0
220-1 | 1 | 1
.
.
.

## Slide 15: Multiple Processes
Process 1 Virtual Address Space (4GB)
Physical Address Space
4 GB Main Memory
(1M Pages)
Process 2 Virtual Address Space (4GB)
PPN 0
PPN 1
PPN 220 -1
- Multiple processes share the same physical memory
- Each process sees a contiguous 32-bit virtual address space, even if physical locations are not contiguos

## Slide 16: Homonyms
The same VA (in different processes) can map to two different physical addresses
Physical Address Space
4 GB Main Memory
(1M Pages)
Process 2 Virtual Address Space (4GB)
PPN 0
PPN 1
PPN 220 -1

## Slide 17: Synonyms
Different VAs can map to the same physical address
Shared code and data
Physical Address Space
4 GB Main Memory
(1M Pages)
Process 2 Virtual Address Space (4GB)
PPN 0
PPN 1
PPN 220 -1

## Slide 18: Address Translation
Page Offset
(12 bits)
Virtual Page Number
(20 bits)
Virtual Address (32 bits)
Page Table
Page Offset
(12 bits)
Physical Page Number
(m bits)
n Byte Main Memory
m = log2(n/4096)
PPN 0
PPN n/4096 - 1

## Slide 19: Translation Look-Aside Buffer (TLB)
Page tables can be large
  64-bit address space with 4KB pages: up to 254 page table entries!
  In practice most processes only use a fraction of VA space => most page table entries are empty
    More complex data-structures to compress page table size
  Bottom-line: expensive to store entire page table on chip and page table look-up can be time consuming
TLBs cache page table entries in a small on-chip hardware structure
  On a miss in the TLB, either hardware or software brings in relevant entry from the page table into the TLB by “walking” the page table

## Slide 20: Address Translation
L1 Cache
L2 Cache
CPU
Main Memory
Address Translation
Main memory accessed using physical addresses
L1 and L2 caches accessed using virtual addresses
Drawbacks of using virtually addressed caches?
  Homonyms: Same VAs map to different PAs. Can the caches distinguish homonyms?
  Synonyms: two VAs map to the same PA. Multiple copies of the same data in the cache
  Solution: Flush caches on a context switch

## Slide 21: Address Translation
L1 Cache
L2 Cache
CPU
Main Memory
Address Translation
Main memory accessed using physical addresses
L1 cache virtually addressed
L2 cache physically addressed
Drawbacks of using virtually addressed caches?
  Homonyms: Same VAs map to different PAs. Can the caches distinguish homonyms?
  Synonyms: two VAs map to the same PA. Multiple copies of the same data in the cache
  Solution: Flush caches on a context switch

## Slide 22: Address Translation
L1 Cache
L2 Cache
CPU
Main Memory
Address Translation
Main memory accessed using physical addresses
L1 cache physically addressed
L2 cache physically addressed
Drawbacks?
  Adds extra latency for TLB look-up before L1 cache access
  Fast, single-cycle L1 access is critical for processor performance

## Slide 23: Address Translation
L1 Cache
L2 Cache
CPU
Main Memory
Address Translation
Main memory accessed using physical addresses
L1 cache virtually indexed but physically tagged
L2 cache physically addressed
Perform address translation in parallel to L1-cache lookup
  Virtually indexed but physically tagged (VIPT) cache!
  Best of both worlds (hopefully)
    Since the L1 cache tags are physical, solves the synonym and homonym problems
    But, address translation does not add extra latency to lookup

## Slide 24: 1 KB Direct Mapped Cache with 1 Byte Blocks
Block 0
Block 1
Block 2
Block 1024
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 1024
Tag Array
(22 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(10 bits)
Physical Tag
(22 bits)
Virtual Address (32 bits)
V 2
=
&
1
HIT
1
VPN
(20 bits)
PPN
(20 bits)
TLB
Physical Tag
(22 bits)

## Slide 25: Homonyms and Synonyms
Index
(10 bits)
Virtual Address (32 bits)
VPN
(20 bits)
PPN
(20 bits)
TLB
Physical Tag
(22 bits)
Homonyms: same VA mapping to different PAs
  Tags bit for the VAs are different so they can be distinguished
Synonyms: different VAs mapping to same PA
  Page offset same for VA and PA
  Index bits are a subset of the page offset
  Therefore, same index bits for both VAs
  And same physical tag
  Hence only one copy of the data in cache
Page Offset
(12 bits)
Page Offset
(12 bits)

## Slide 26: 32 KB direct mapped cache
Index
(15 bits)
Virtual Address (32 bits)
VPN
(20 bits)
PPN
(20 bits)
TLB
Physical Tag
(17 bits)
Problem here is that the index is larger than the page offset!
Homonyms: same VA mapping to different PAs
  Tags bit for the VAs are different so they can be distinguished
Synonyms: different VAs mapping to same PA. Is this a problem?
  Yes: index bits are derived from both the page offset and the VPN
  Data from the same PA can end up in different locations in the cache
Page Offset
(12 bits)
Page Offset
(12 bits)

## Slide 27: Midterm Review

## Slide 28: 0/1/2 Address ISAs
“2-Address” ISA
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
“1-Address” ISA
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator
STACK
TOS
ALU
(+, -, x)
Accumulator
“0-Address” ISA

## Slide 29: How is Memory Accessed
Memory can also be bit-addressable, 32-bit addressable, 64-bit addressable, etc.
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
Addr
Mem[Addr]
“Byte addressable”
How many bits should Addr have?
{Mem[Addr], Mem[Addr+1], Mem[Addr+2], Mem[Addr+3]}

## Slide 30: Load-Store ISA
Instructions like add, sub etc. operate only on registers (examples: MIPS, ARM, 3/2/1/0-Address ISAs we have seen so far)
  Separate Load/Store instructions to fetch data from memory into registers and to write data back from registers to memory
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
add rs, rt, rd
($rd ←$rs + $rt)
load rt, M
($rt ←Mem[M])
store rt, M
( Mem[M] ←$rt )
Load data at memory location M
into register rt
Store data in register rt to memory location M

## Slide 31: Addressing Modes
How to specify where to read from/write to
Orthogonal ISA: each op supports every addressing mode (ex: VAX)
load rt, M
($rt ←Mem[M])
Absolute
load rs, rt
($rt ←Mem[$rs])
Register Indirect
load rs, rt, offset
($rt ←Mem[offset+$rs])
Displaced/Based
Directly provide memory address
Memory address from register rs
Add an offset to address stored in register rs
load rs, rt, rd
($rd ←Mem[$rs + $rt])
Indexed
load rt, rs
($rt ←Mem[Mem[$rs]]
Memory Indirect
load rt, rs
($rt ←Mem[$rs]
$rs ←$rs + 1)
Auto-increment
Base memory address and offset from registers
Use value at Mem[$rs] as address
Same as Register indirect + value in rs is automatically incremented

## Slide 32: Memory-Memory ISA
Allow instructions like add/sub to operate directly on data in memory (Examples include: x86, VAX etc.)
Most generally, each of the two operands and the result can be read-from/written-to either memory or register file
  Pros?
  Cons?
add Ms, Mt, Md
(Mem[Md] ←Mem[Ms] + Mem[Mt])
Memory address

## Slide 33: 2’s Complement Representation
add rs, rt, rd // R[rd] ← R[rs] + R[rd]; signed addition; trap on overflow
rs, rt and rd are assumed to contain 32-bit signed, 2’s complement numbers
Example using 4-bit signed complement numbers ([-8,7])
Overflow occurs when result lies outside [-8,7]
1 1 0 1 = -1*23 + 1*22 + 0*21 + 1*20 = -8 + 4 + 0 + 1 = -3
+ 1 1 0 1 = 0*23 + 1*22 + 0*21 + 1*20 = 0 + 4 + 0 + 1 = -3
-----------
1 1 0 1 0 = 0*23 + 0*22 + 1*21 + 0*20 = 0 + 0 + 2 + 0 = 2
Carry out
bit is dropped

## Slide 34
//Original instruction
add rs, rt, rd //R[rd] <- R[rs] + R[rt]
// x = a + b = a – (0-b)
//Pseudo-code
maxval = 32’b1
If (rs==maxval)
If (rt==maxval)
Rx = 32’b1
addi rx, rd, 1
Else
subu $0, rt, rx
Sub rs, rx, rd
Else
Subu $0, rs, rx
Sub rt, rx, rd

## Slide 35: MIPS Instructions: J-Type
j address // PC ← {PC+4[31:28], address, 00}
(Error in Lecture 2)
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
Immediate operand
j: 2hex
jal: 3hex
// imm1 = {PC+4[31:28], address[25:14]}
// imm2 = {address[13:0],00}
lui rx, imm1 //R[rx] = {imm1, 16’b0}
ori rx, rx, imm2 //R[rx] = {imm1,imm2} (i.e., the target address for the j instruction
jr rx

## Slide 36
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
Sign
Extend
15:0
I-Type?
I-Type?
PC
Read Address
Instruction
Instruction Memory
Adder
+4
Concat
31:28
PC+4
25:0
00
NextPC? = function(J-Type?, IsBranch?, IsEq?)
Adder
PC+4
=
IsEq?
{SignExtendImm[29:0],00}
29:0
3:1 MUX
Final Data-Path (Instruction Fetch)
What would you do on an I-cache miss?

## Slide 37
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Final Data-Path (Reg Rd/Execute/Mem/Write-back)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?

## Slide 38
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
What would need to change to add support for memory indirect loads? (Mem[Mem[$rs]])
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?

## Slide 39: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5
EX-EX Forwarding

## Slide 40: RAW Hazards: Add-Add Dependency (What if EX stages takes 2 clocks?)
IF
ID/RF
EX1
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
t5
IF
ID/RF
EX1
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5
EX2-EX2 Forwarding? How to fix this?
MEM
nop
WB
Write $3
EX2
R[$1] + R[$2]
EX2
R[$3] + R[$4]

## Slide 41: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5

## Slide 42: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Will this work?
Solution: Stall the pipeline

## Slide 43: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Solution: Stall the pipeline
EX
R[$4] + R[$5]

## Slide 44: RAW Hazards: Load-Store Dependency (What happens on a D-cache miss?)
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
R[$4] = Mem[Addr]
WB
Write $4
IF
ID/RF
EX
MEM
sw $5, $4, imm
Read $5
Mem[Addr] = R[$4]
WB
Write $9
MEM-MEM Forwarding (new)
Addr = R[$5] + SgnImm