## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Out-of-Order Processing
Instructor: Siddharth Garg

## Slide 2: Lab 2 Overview
You will model a two level cache hierarchy
L1
L2
Main Memory (always HIT)
Replacement policy: round-robin
Write Hit policy: write-back
Write Miss policy: no-allocate
Rd A
Hit
L1 Cache Event | L2 Cache Event
Rd Hit | No Access

## Slide 3: Lab 2 Overview
You will model a two level cache hierarchy
L1
L2
Main Memory (always HIT)
Replacement policy: round-robin
Write Hit policy: write-back
Write Miss policy: no-allocate
Rd A
Rd Miss
L1 Cache Event | L2 Cache Event
Rd Miss | Rd Hit
Rd A
Rd Hit
Mem[A]
Eviction
(Wrt B)
Wrt Hit (Dirty bit updated but no further eviction)
Wrt Miss (L2 bypassed)

## Slide 4: Variable Execution Latency
IF
ID/RF
EX
MEM
WB
5-Stage Pipeline
But in Reality…
IF
ID/RF
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
EX
INT ALU
INT MUL
FP MUL
LD
(on miss)
MEM
WB
.
.

## Slide 5: WAW Hazard
Assume FP add has 3 cycle latency, FP mult has 6 cycle latency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
IF
ID/RF
EX
EX
EX
EX
EX
EX
MEM
WB
IF
ID/RF
EX
EX
MEM
WB
mul
Rd $f1, $f2
Wrt $f3
nop
add
Rd $f4, $f5
Wrt $f3
Write-after-Write
(WAW) Dependency
What’s the final value in $f3?
EX

## Slide 6: Potential Solution: Stalling
Assume FP add has 3 cycle latency, FP mult has 8 cycle latency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
IF
ID/RF
EX
EX
EX
EX
EX
EX
MEM
WB
IF
ID/RF
EX
EX
MEM
WB
mul
Rd $f1, $f2
Wrt $f3
nop
add
Rd $f4, $f5
Wrt $f3
STALL
EX

## Slide 7: Impact on ILP
Assume FP add has 3 cycle latency, FP mult has 8 cycle latency
Future independent add instructions stall because of the WAW dependency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
add.d $f8, $f6, $f7 // R[$f8] = R[$f6] + R[$f7]
add.d $f11, $f9, $f10 // R[$f11] = R[$f9] + R[$f10]

## Slide 8: Solutions
Use another destination register to eliminate WAW haa
  But number of architectural registers is limited
Out-of-order (OoO) execution in hardware
  Allows independent instructions whose operands are ready to execute first
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f12 // R[$f3] = R[$f4] + R[$f5]
add.d $f8, $f6, $f7 // R[$f8] = R[$f6] + R[$f7]
add.d $f11, $f9, $f10 // R[$f11] = R[$f9] + R[$f10]

## Slide 9: Enabling OoO Execution
Register renaming in hardware
  Associate a “tag” with the output of each instruction
  Number of tags can be larger than number of architectural regs
Need to buffer instructions till they are ready to execute
  Fetched in order and buffered in “reservation station”
Need to check when an instructions operands are ready
  Each instruction broadcasts its tag when it finishes execution
  Instructions compare their “source tags” (tags of their operands) to see if there is a match
When all source operands of an instruction are ready, dispatch to FU
  Structural hazard if FU is busy

## Slide 10: Tomasulo’s Algorithm
Instruction fetched in order into instruction buffer
And dispatched to reservation station assuming one is free
Instruction wait in reservation stations and monitor common data bus for operand to be available
Arch register file renamed using resv stations

## Slide 11: Register Renaming
Reservation Station
a
b
c
d
Each entry in a reservation station has a tag
When an instruction is assigned to a reservation station, the destination register for that instruction is renamed to the tag of the reservation station
  Architectural registers -> physical registers
  More reservation stations than architectural registers
After renaming, the RS tag is used to refer to that register
Tag

## Slide 12: Register Rename Table
Tag | Value | Valid
 |  | 0/1
One entry for each architectural register
f0
f1
f2
f3
f4
The reservation station entry the register f4 is currently
remapped to
Alternatively, if register is currently not mapped to a reservation station and holds valid data, valid bit is set to 1
Current value of f4 (only if valid bit is set)

## Slide 13: Reservation Station
Tag | Value | Valid
 |  | 0/1
a
b
c
d
Tag from which the value of operand 1 will be obtained
Tag | Value | Valid
 |  | 0/1
Set if value is valid
Value

## Slide 14: Tomasulo’s Algorithm
If a reservation station is available before renaming
  Instruction + renamed operands (tags/value) placed in reservation station
  If reservation station not available, STALL
While in resv stn each instruction
  Monitors CDB for tag of it’s sources
  When tag seen, grab value and keep in the reservation station
  When values for both operands available, ready for dispatch
Dispatch ready instructions to Fus
  Assuming an FU is available, otherwise wait
Once instruction completes execution
  Broadcast value and tag on CDB
  Any Register in the Reg. renaming table with a matching tag updates it value and sets valid bit
Free reservation station

## Slide 15: Example
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F
D
EX
W
F: Fetch instruction
D: Decode, Rename
E: Execute (when operands ready), multi-cycle
W: Broadcast result on CDB

## Slide 16: Example
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F
D
EX
WB
F: Fetch instruction
D: Decode, Rename
E: Execute (when operands ready), multi-cycle
WB: Broadcast result on CDB

## Slide 17: Cycle 0
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
 |  | 0
 |  | 0
x
y
Tag | Value | Valid
 |  | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5

## Slide 18: Cycle 1
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
 |  | 0
 |  | 0
x
y
Tag | Value | Valid
 |  | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F

## Slide 19: Cycle 2
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
~ | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
~ | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
D
F
Resv Stn x ready to execute

## Slide 20: Cycle 3
Tag | Value | Valid
x | ~ | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
~ | 4 | 1
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
~ | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
~ | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
D
F
E1

## Slide 21: Cycle 4
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
 |  | 0
 |  | 0
Tag | Value | Valid
-- | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
-- | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD 43 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11,
W
D
E2
F
Resv Stn b ready to execute

## Slide 22: Cycle 5
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
 |  | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
 |  | 0
Tag | Value | Valid
-- | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
-- | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
E1
E3
F
D
Resv Stn c ready to execute

## Slide 23: Cycle 6
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
 |  | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
 |  | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
E2
E4
F
E1
D

## Slide 24: Cycle 7
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
E3
E5
D
E2
W
Note that f5 is remapped from a to d

## Slide 25: Cycle 9
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8

## Slide 26: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
~ | 8 | 1
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
Update all resv stn entries
waiting for tags x and b

## Slide 27: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
~ | 8 | 1
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
~ | 2 | 1
 | .. | ..
d | .. | 0
~ | 8 | 1
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
Update RF entries currently mapped
to tags x and b

## Slide 28: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | ~ | 0
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | ~ | 0
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | ~ | 0
~ | 8 | 1
x
y
Tag | Value | Valid
~ | ~ | 0
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
Release resv. stns x and b
Resv station a is ready to be scheduled!

## Slide 29: Future Cycle
Tag | Value | Valid
~ | 2 | 1
~ | ~ | 0
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | ~ | 0
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | ~ | 0
~ | 8 | 1
x
y
Tag | Value | Valid
~ | ~ | 0
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
WB
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
When resv a completes execution, its value is sent to operand in resv stn d but not updated in RF. Why?

## Slide 30: Data-Flow Representation
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
*
f1
f2
f3
+
f4
+
f2
f6
f7
+
f8
f9
f10
*
+
+
f5
f11
0
0
0
0
0
0
4
4
6
8
10
14
Out-of-order execution attempts to reconstruct the data-flow graph on the fly

## Slide 31: Scheduler Design
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
 |  | 0
 |  | 0
x
y
Tag | Value | Valid
 |  | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f3, f6, f7

## Slide 32: Cycle 8
Tag | Value | Valid
x | ~ | 0
x | ~ | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
~ | 4 | 1
~ | 6 | 1
 |  | 0
 |  | 0
Tag | Value | Valid
~ | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
~ | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f3, f6, f7
E6

## Slide 33: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
~ | 4 | 1
~ | 6 | 1
 |  | 0
 |  | 0
Tag | Value | Valid
~ | ~ | 0
 |  | 0
x
y
Tag | Value | Valid
~ | ~ | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
~ | 2 | 1
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f3, f6, f7
WB
Both reservation stations are ready to execute. Which one should be executed first?
  Oldest first? Most dependencies?

## Slide 34: Multiple EX Units
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
~ | 4 | 1
~ | 6 | 1
 |  | 0
 |  | 0
Tag | Value | Valid
~ | ~ | 0
 |  | 0
x
y
Tag | Value | Valid
~ | ~ | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
~ | 2 | 1
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f3, f6, f7
WB
FP ADD (4 cycles)
Execute both addd instructions in parallel!

## Slide 35: Exceptions
Exceptions are interrupts generated by the processor when critical events occur that require special handling
  Arithmetic overflow (recall add instruction)
  Page fault
  Mem protection violation
Out-of-order execution beyond branches can cause exceptions that would not be caused by in order execution
  If for example a branch predicted as Taken is actually Not Taken
Precise exceptions: architectural state of the processor correspond to in-order execution of program till instruction that raised exception

## Slide 36: Dealing with Exceptions in Tomasulo
Instructions are only allowed to execute if all prior branch instructions have resolved
  Or, speculate past branches but “mute” exceptions till the branch is resolved
However, there is still a problem with precise exceptions
  Note that Tomasulo’s algorithm updates the register file out of order
  An older instruction might raise an exception even though a younger instruction has already update the RF contents
    Or yet older instructions haven’t yet updated the RF